BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Parks and Open Space Maintenance

BMP Title: Fountain & Pool Maintenance

BMP Description: Use chlorine or other alternatives to control algae, not copper-based algaecides. Drain water from fountains and pools to a sanitary sewer or water can be dechlorinated and recycled/reused by draining it gradually onto a landscaped area. Water is tested to ensure no chlorine present. Maintain an ‘air gap’ between the discharge line and the sewer line to prevent backflow to the sanitary sewer. Provide drip pans beneath drain pipe connections to prevent leaks. Never clean a filter in the street or near a storm drain. Rinse cartridge filters onto a dirt area and spade filter residue into soil. If there is not a proper dirt area for discharge, filter backwater to the sanitary sewer if permitted.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Parks and Open Space Maintenance

BMP Title: Lakes, Ponds and Lagoon Maintenance

BMP Description: Reduce fertilizer use around the water body. Discourage the public from feeding the wildlife to control bacteria. Consider introducing fish that eat algae. Educate the public on algae and relay that certain types of algae are beneficial to the water. Control erosion in many ways such as maintaining vegetative cover on banks, provide riprap along banks so minimize erosion potential, and confine excavated materials away from lakes and keep covered. Conduct inspections to detect illegal dumping in or near a lake. Pickup landscape waste in and around lakes where feasible. Provide and maintain trash cans near recreational water bodies for the public, and increase trash collection during peak visitation.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Parks and Open Space Maintenance

BMP Title: Landscape Maintenance

BMP Description: Use mechanical methods of vegetation removal whenever possible. Avoid loosening the soil when removing weeds, and use mulch when soils are exposed. Collect lawn and grass clippings, pruning waste, tree trimmings and weeds, and compost or dispose of properly. Place stockpiles away from water and berm or cover them to prevent releases to the storm drains. Consider planting native vegetation where feasible. Reduce the use of high nitrogen fertilizers which produce excess growth. Avoid placing landscape waste around storm drain inlets. Only irrigate when needed and use measures to ensure minimal runoff. Utilize a management system that incorporates integrated pest management techniques. Use pesticides only if there is an actual problem. Do not use pesticides if rain is expected, and do not prepare pesticides near a storm drain. Calibrate application equipment to avoid excessive application. Fertilizers should be worked into the soil rather than left on the surface, and sweep fertilizer off pavement before watering. Dispose of containers accordingly.

Measurable Goals: Report percent of staff applying pesticides who are NYS Certified Applicators. Reduction in fertilizer usage. Reduction in pesticide usage and adoption of alternative pest control approaches.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Parks and Open Space Maintenance

BMP Title: Outdoor Storage of Raw Materials

BMP Description: Store all materials inside. If this is not feasible, then all outside storage areas should be covered with a roof and enclosed to prevent storm water contact. Cover and contain stockpiles of raw materials while not in use to prevent storm water from running into the covered piles. If stockpiles are to large to be covered and contained, implement erosion control practices at the perimeter of the site. Keep liquids in a designated area on a paved impervious surface with secondary containment. Keep outdoor storage containers in good condition, and in a clean and dry area. Secure drums stored in an area to prevent accidental spillage or stealing. Cover wood treated with chromated copper arsenate, ammonical copper zinc arsenate, creosote, or pentachlorophenol with tarps store indoors. Store chemicals, drums, or bagged materials in secondary containers if applicable. Release accumulated stormwater in petroleum storage areas prior to the next storm. Water should at least pass through an oil/water separator and, if allowed, discharged to a sanitary sewer.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Parks and Open Space Maintenance

BMP Title: Pet Waste Collection

BMP Description: Assess municipal parks and open space areas to determine locations with excessive amounts of pet waste. Prioritize problem areas based upon quantity of pet waste and proximity to waterbodies. Install pet waste signs or bag stations as necessary.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail: