DESCRIPTION

This work shall consist of providing all of the labor and equipment  to excavate existing  shoulders of various materials (to the widths and depths indicated by the item) utilizing a milling machine.  The intent of this item is to perform production milling/excavation on County roads.  The County will provide maintenance and protection of traffic in conjunction with all of the  operations.  Due to limitations of the existing pavement width, most shoulders will be excavated one side at a time to allow for backfilling and proper traffic maintenance.  The provisions of NYSDOT Standard Specifications, Section 203, latest revision, shall apply except as modified herein.

MATERIALS

None Specified.

CONSTRUCTION DETAILS

The construction details of NYSDOT Standard Specifications, Subsection 203-3, latest revision, shall apply with the following modifications:

- The excavation MUST be performed by a milling machine.

- The County will coordinate and provide the relocation and/or removal of mailboxes, sign posts, etc. to provide a clear path for the milling machine to operate.

- Maintenance and protection of traffic will be provided by others.

- Excavated material must be disposed of if trucking is included in the item.

- Refer to the attached detail for typical excavation sections.

METHOD OF MEASUREMENT

The method of measurement of NYSDOT Standard Specifications, Subsection 203-3, latest revision, shall apply with the following modifications:

The quantity to be paid for shall be the number of linear feet of shoulder milled at the specified width and depth as specified by the item.  The unit price shall include a mobilization cost for the work.  In the event the contractor is required to remobilize, the appropriate remobilization bid item will be paid.

BASIS OF PAYMENT

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C203.81 | Shoulder Excavation – Milling (8”-10” depth, including trucking, 4’ wide) | LF |
| C203.82 | Shoulder Excavation – Milling (10”-12” depth, including trucking, 4’ wide) | LF |
| C203.83 | Shoulder Excavation – Milling (8”-10” depth, including trucking, 6’ wide) | LF |
| C203.84 | Shoulder Excavation – Milling (10”-12” depth, including trucking, 6’ wide ) | LF |
| C203.85 | Shoulder Excavation – Milling (8”-10” depth, without trucking, 4’ wide) | LF |
| C203.86 | Shoulder Excavation – Milling (10”-12” depth, without trucking, 6’ wide) | LF |
| C203.87 | Shoulder Excavation – Milling (8”-10” depth, without trucking, 6’ wide) | LF |
| C203.88 | Shoulder Excavation – Milling (10”-12” depth, without trucking, 6’ wide) | LF |
| C203.89 | Shoulder Excavation – Remobilization | LS |